## Slide 1
Hierarchical Multi-Agent Reinforcement Learning for Congestion-Aware Maritime Scheduling
Project update: simulator background, reward redesign, controlled validation benchmark, current progress, and next steps.
We now have both a strong continuous baseline and a controlled benchmark for validating the core control logic before reintroducing forecast uncertainty.
SPRING 2026
Independent study
Supervisor: Prof. Amine Aboussalah
MARCH 31 UPDATE
Baseline: v3 + GT benchmark
RESEARCH FOCUS
HMARL
Coordinator, vessel, and port agents
CURRENT SETUP
v3 + GT
Operating baseline plus validation benchmark
FORMAT
12 slides
Presentation-ready update deck

## Slide 2
CONTEXT
Why this project matters
02
Operational context
Ports have limited berth capacity and nonzero service time.
Vessels trade off speed, fuel burn, emissions, and lateness.
Poor local choices can create downstream congestion and idle capacity elsewhere.
The system is naturally multi-agent, asynchronous, and resource-constrained.
Congestion
Too many arrivals to one port can create queueing and delay at the whole network level.
Cost
Faster sailing can improve timing but increases fuel use, emissions, and operating cost.
Coordination
Ports and vessels need global guidance, not only local reactive behavior.
Research value
This is a strong testbed for hierarchical coordination under delayed information.

## Slide 3
QUESTIONS
What we are trying to learn
03
Umbrella question
Can hierarchical MARL improve maritime scheduling under congestion and resource constraints?
RQ1
How can heterogeneous agents coordinate using shared congestion forecasts?
RQ2
Does proactive coordination improve over independent and reactive baselines?
RQ3
Which forecast horizons and sharing strategies maximize decision quality?
RQ4
How do coordination improvements affect fuel, delay, and carbon cost?
The project is organized around a chain of related questions: coordination, baselines, forecast design, and economics.

## Slide 4
ENVIRONMENT
Current simulator setup
04
Topology
5 ports, 8 vessels, 3 docks per port
Time scale
1 hour per step and 6 hour default service time
Travel
Synthetic port-distance matrix with routes from 22 to 98 nautical miles
Fuel
Default fuel is 100, with refueling only after real service completion
Synthetic port distance matrix (nautical miles)
Rows and columns are ports P0–P4; the diagonal is 0, and the matrix is symmetric.
The values are synthetic and scaled so multiple voyages can complete within one rollout.
P0
P1
P2
P3
P4
P0
0
84
22
34
78
P1
84
0
98
61
54
P2
22
98
0
55
59
P3
34
61
55
0
82
P4
78
54
59
82
0

## Slide 5
EXPERIMENT
How the current baseline is trained and evaluated
05
Main operating baseline
Algorithm: MAPPO with centralized training and decentralized execution
Parameter sharing across vessels and across ports
100 training iterations and rollout_length = 64
Environment horizon = 69
Seed = 42
Local CPU run for the reported baseline
Controlled validation benchmark
single_mission episodes
ground_truth forecasts
Each vessel completes at most one trip per episode
Used to validate control logic before reintroducing forecast error
Primary evaluation metrics
On-time rate
Completed arrivals
Vessels served
Dock utilization
Total operating cost

## Slide 6
ARCHITECTURE
Three decision layers with delayed coordination
06
Fleet coordinator
Strategic destination guidance Slowest decision cadence
Vessel agents
Speed control Arrival-slot requests
Port agents
Request acceptance Service and berth decisions
→
→
The environment is intentionally asynchronous, so the policies must coordinate under delayed information and physical travel time.

## Slide 7
MECHANICS
How one simulation step works
07
Transition kernel
1. Deliver messages
Apply due actions and delayed communications.
2. Advance vessels
Update motion, fuel burn, emissions, and arrivals.
3. Process ports
Update queue, berth service, service completion, and refueling.
4. Compute rewards
Log diagnostics and compute role-specific rewards.
Why this matters
The environment is not one big update; it moves through communication, travel, berth service, and reward calculation in sequence.
This is why delays, arrivals, and service completions show up at different times in the logs.
The next two slides separate reward intuition from reward formulas so the audience sees both the story and the technical definition.

## Slide 8
REWARDS
Reward structure in plain language
08
Vessel reward
Reward = arrival and punctuality minus travel cost
What it rewards
Arrival, On-time arrival
What it penalizes
Fuel used, Delay added, CO2 emitted, Transit time, Schedule delay
Port reward
Reward = responsive berth management minus congestion cost
What it rewards
Accepted requests, Vessels served
What it penalizes
Rejected requests, Queue waiting, Idle docks
Coordinator reward
Reward = system flow and utilization minus network-wide cost
What it rewards
Accepted requests, Vessels served, Berth utilization
What it penalizes
Fuel, Queue, Idle docks, Delay, Schedule delay, CO2, Rejected requests
This is the audience-facing summary. The next slide shows the actual symbolic formulas used in the simulator.

## Slide 9
REWARDS
Actual reward formulas used in the simulator
09
Symbolic form
Vessel reward
r_V(t) = r_arr·1[arrived] + r_on·1[on_time] − (w_fΔfuel + w_dΔdelay + w_eΔCO2 + w_tΔtransit + w_sΔsched)
Port reward
r_P(t) = r_acc·accepted + r_srv·served − r_rej·rejected − (queue·dt + w_idle·idle_docks)
Coordinator reward
r_C(t) = r_acc·accepted + r_srv·served + r_util·avg_occupied − (w_fΔfuel + w_qavg_queue + w_iavg_idle + w_dΔdelay + w_sΔsched + w_eΔCO2 + r_rej·rejected)
Δ terms are per-step increments; accepted, rejected, and served are event counts for the current step.

## Slide 10
PROGRESS
What changed since March 6
10
Corrected vessel behavior
No more collapse to constant minimum speed. Requested arrival times now become real schedule deadlines.
Fuel and stalling
Fuel exhaustion now causes true mid-route stalling. Departures are checked for fuel feasibility.
Port service realism
Ports track actual vessel IDs. Refueling happens after real service completion.
Reward redesign
Rewards moved from mostly aggregate penalties to event-driven, role-specific signals.
Validation variants
Added single_mission and ground_truth as controlled debugging modes.
Visibility
Action logs, event logs, reward components, and confidence diagnostics were added.

## Slide 11
DIAGNOSTICS
Why the current results are more trustworthy
11
Transparency upgrades
Grouped plots separate aggregate, vessel, port, and coordinator behavior.
Per-step eval trace, action log, and event log are available.
Reward-component decomposition shows which terms dominate.
Policy-confidence metrics make near-uniform coordinator behavior easier to diagnose.
Role-specific reward traces over one evaluation episode. We show all three because vessel, port, and coordinator each optimize a different part of the task.
TRACE FILE
eval_trace.csv
ACTION LOG
eval_action_trace.csv
EVENT LOG
eval_event_log.csv

## Slide 12
BASELINE
Current recommended baseline: transit-rebalanced v3
12
Preferred operating balance
TOTAL REWARD
-923.38
ON-TIME RATE
0.928
COMPLETED ARRIVALS
26.8
VESSELS SERVED
36.2
DOCK UTILIZATION
0.28
OPS COST
$1.330M

## Slide 13
BENCHMARK
Continuous task vs. single-mission validation benchmark
13
Continuous + ground truth
EVAL TOTAL REWARD
-673.99
ON-TIME RATE
0.759
COMPLETED ARRIVALS
14.8
VESSELS SERVED
24.2
MISSION SUCCESS
0.0
TRACE STEPS
37
Single mission + ground truth
EVAL TOTAL REWARD
-481.51
ON-TIME RATE
0.575
COMPLETED ARRIVALS
8.0
VESSELS SERVED
9.4
MISSION SUCCESS
1.0
TRACE STEPS
24
Takeaway
The simplified benchmark is easier to complete and gives a cleaner success signal, but the continuous setting still has higher throughput and remains the real target environment.

## Slide 14
NEXT STEPS
What is simplified, and what comes next
14
1. Keep v3
Use transit-rebalanced v3 as the working continuous baseline.
2. Use the benchmark
Use single_mission + ground_truth as the controlled validation benchmark.
3. Compare across seeds
Run short multi-seed comparisons in both settings.
4. Reintroduce uncertainty
Bring back imperfect forecasting after validating control behavior.
5. Decide on realism
Then decide whether to move to real ports and nautical distances.
The short-term goal is not to replace the continuous environment, but to validate the control logic under cleaner conditions.